# APPLICATION NOTE 5: ATHANA MODEL 40-100A DATA CARTRIDGE

For the HP model 85 , when used with Athana model 40-100A data cartridge.

The tape in the Athana model 40-100A data cartridge has a slightly higher coercive force than the tape in the original HP 98200A cartridges. In order to properly overwrote previously written data in the 40-100a cartridges the head write current of the CTU has to be increased.  This can be accomplished by paralleling a 2000 ohm ¼ watt resistor across the 660 ohm write current limiting resistor. The attached drawing shows the location of the write current limiting resistor on the HP00085-60003 board (D-2034) of the CTU.